## Slide 1
Advanced Beam Design
COMPOSITE BEAM
AISC Manual -16th Edition
Developed by Scott Civjan
University of Massachusetts, Amherst
Teaching Modules for
Steel Instruction

## Slide 2
  Chapter I:
  Composite Member Design

## Slide 3
Slab effective width, be
Section I3.1a
To each side of the beam, be is limited by:
one-eighth beam span
one-half distance to adjacent beam
distance to edge of slab
Lowest value controls.

## Slide 4
Metal Deck Slab – Section I3.2c
wr ≥ 2”
tc ≥ 2”
hr ≤ 3”
≥1.5”
≥0.5”
wr = average deck width
hr = height of deck
tc = thickness of concrete above the deck
steel beam
Notes: 4

## Slide 5
Fully Composite Beam:
Bending Strength

## Slide 6
fb = 0.90 (Wb = 1.67)
Bending Strength

## Slide 7
POSITIVE MOMENT
For h/tw
The strength is determined as the plastic stress distribution of the composite section.
(*Note: All current ASTM A6 W, S, and HP shapes satisfy this limit.)
NEGATIVE MOMENT
It is typically assumed that the concrete carries no tensile forces and reinforcement is minimal, therefore strength is identical to a bare steel section.
Bending Strength

## Slide 8
INSERT INFORMATION: STRENGTH OF FULLY COMPOSITE BEAM SECTION CALCULATIONS
Handout on Calculations:
FullyCompositeCalcs.PDF

## Slide 9
Fully Composite Strength can be determined by using Table 3-18.
Y2 - Calculated per handout
Y1 = 0 if PNA in the slab,
Calculated per handout if PNA in the beam flange or web.
Bending Strength

## Slide 10
Table 3-18 Nomenclature
(page 3-15)
be
a
Ycon
a/2
Y2
Location of effective concrete flange force (SQn)
TFL(pt.1)
BFL(pt.5)
6
7
Y1 = Distance from top of steel flange to any of the seven tabulated PNA locations
4 Eq. spaces
1
2
3
4
5
TFL
BFL
tf
Beam Flange Enlarged Detail
1
5

## Slide 11
To reach fully composite strength,
shear studs must transfer SQn for Y1 = 0 (maximum value) listed in Table 3-18.
This is equivalent to value C* in calculations (handout).
Bending Strength

## Slide 12
Shear Stud Strength

## Slide 13
limits value to strength of individual shear studs.
Strength of each stud, Qn
Equation I8-1
limits value to crushing of concrete around the shear stud.
Notes: Note that this indicates that push-out of a stud through a rib could be minimized by increasing Fu of the stud, which is not realistic. The equations assume standard materials.

## Slide 14
Asa = cross-sectional area of shear stud
Ec = modulus of elasticity of concrete
Fu = shear stud minimum tensile strength
(typically 65ksi)
Rg accounts for number of studs welded in each deck rib and wr/hr.
Values are 1.0, 0.85, or 0.7.
Rp accounts for deck rib orientation with respect to the beam, stud engagement in the concrete above the rib, and weak or strong stud location.
Values are 0.75 or 0.6.

## Slide 15
Strength, Qn, for one shear stud
Table 3-20

## Slide 16
Limitations on shear stud placement
for shear studs placed in metal decking:
Section I8.2d
Center-Center Spacing: > 4 times diameter
≤ 8 times slab thickness
≤ 36 inches
Section I8.1
Shear Stud Diameter: ≤ 3/4”
≤ 2.5 times flange thickness unless over web

## Slide 17
Composite strength requires that shear studs transfer SQn to each side of the maximum moment in the span.
If SQn strength of the shear studs is inadequate to provide fully composite action, the beam is partially composite.

## Slide 18
Partially Composite Beam:
Bending Strength
fb = 0.90 (Wb = 1.67)

## Slide 19
INSERT INFORMATION: STRENGTH OF PARTIALLY COMPOSITE BEAM SECTION CALCULATIONS
Handout on Calculations:
PartiallyCompositeCalcs.PDF

## Slide 20
Partially Composite Strength can be determined by using Table 3-18.
Y1 - Calculated per handout
Y2 - Calculated per handout

## Slide 21
Partially Composite Action is limited by the total strength of shear studs.
SQn listed in Table 3-18.
This is equivalent to value C* in calculations (handout).

## Slide 22
Composite Beam: Shear Strength

## Slide 23
SHEAR STRENGTH
It typically is assumed that the slab carries no shear forces. Therefore, strength is identical to a bare steel section.

## Slide 24
Composite Beam
Deflection Calculations

## Slide 25
Itr = transformed section moment of inertia
Lower bound values of Itr are found in Table 3-19 (ILB).
Values assume concrete area equal to SQn/Fy rather than actual area.
Deflection Calculations
Fully Composite

## Slide 26
Deflection Calculations
Partially Composite
Iequiv = effective moment of inertia
Is = moment of inertia of steel section only
Itr = fully composite moment of inertia
ΣQn = sum of the nominal strengths of the steel anchors between the point of maximum moment to the point of zero moment
Cf = fully composite shear transfer force
Equation C-I3-3

## Slide 27
Deflection Calculations
Partially Composite
Equation C-I3-4
Seff = effective elastic section modulus
Ss = elastic section modulus of steel section only
Str = fully composite elastic section modulus
ΣQn = sum of the nominal strengths of the steel anchors between the point of maximum moment to the point of zero moment
Cf = fully composite shear transfer force

## Slide 28
Deflection Calculations
Partially Composite
Table 3-19 can be used for
lower bound values of Iequiv.