## Slide 1
Teaching Modules for
Steel Instruction
Advanced Beam
FATIGUE THEORY SLIDES
Developed by Scott Civjan
University of Massachusetts, Amherst

## Slide 2
Fatigue - Definitions
Typical of bridge loading, vibrating equipment,
wind loading on signage.
High Cycle Fatigue
Formation of a crack due to cyclic elastic loading
below design stress levels.
20,000 to millions of cycles

## Slide 3
Fatigue - Definitions
Typical of seismic loading of connections.
NOT COVERED IN THE FOLLOWING SLIDES
Low Cycle Fatigue
Formation of a crack due to cyclic inelastic loading.
Less than 20,000 cycles to failure

## Slide 4
Prefer ductile failures if fracture occurs.
Brittle Fracture
Sudden failure, often with minimal plastic deformation.
Ductile Fracture
Progressive failure, often with minimal plastic deformation.
Fatigue - Definitions

## Slide 5
Brittle Fracture
More likely with:
Stress Concentrations
High Constraint
High Load Rate
Low Material Toughness
Low Temperature
Fatigue - Definitions

## Slide 6
Stress
Time
1 cycle
Stress range
For a constant amplitude stress range
Stress Range: The difference between maximum
and minimum stress values.
Cycle: one application and unloading of stress range.
Fatigue - Definitions

## Slide 7
To predict the fatigue life, S-N curves typically are used.
These are log-log plots of stress range versus number of cycles expected to cause fatigue fracture.
Fatigue - Definitions

## Slide 8
Linear Relationship for design life on log-log plot
Stress Range (log scale)
Number of Cycles (log scale)
Threshold Stress Range
S-N Curve
Fatigue Life
Fatigue - Definitions

## Slide 9
Fatigue Life: The number of stress cycles to cause fracture.
Threshold Stress Range: A stress range below which fatigue life is expected to be infinite.
Fatigue - Definitions

## Slide 10
Design Life: The expected number of stress cycles applied.
Design Category: A grouping of design details with similar fatigue parameters, such as stress concentrations and constraints.
The S-N curve can be related to the actual stress range and expected design life.
Fatigue - Definitions

## Slide 11
Fsr = Design stress range
N = Design life
Fth = Threshold stress range
Cf = Constant dependent on design category
Typical equation for steel design is shown. Others exist for different conditions or materials.
Fatigue - Design

## Slide 12
Given a detail and design life, can calculate the allowable stress range.
Given a detail and applied stress range, can calculate the design life.
Fatigue - Design

## Slide 13
Unfortunately, the stress range history for a given structure typically is irregular unless fatigue is caused by machinery.
Need to transform irregular stress range pattern into an equivalent constant amplitude stress range.
Fatigue - Design

## Slide 14
Transferring Variable Amplitude Stress Ranges to Constant Amplitude Stress Range
Miner’s Rule
Fsr = Design Stress Range
ai = number of cycles at stress range Fsri divided by the total number of cycles
Fsri = Individual stress range within load history
Fsrmax = Maximum stress range within load history
Fatigue - Design

## Slide 15
Finite life if Fsr>Fth
Base fatigue life on S-N curve.
Infinite life if Fsr ≤ Fth AND Fsrmax ≤ Fth.
Finite life if Fsr ≤ Fth but Fsrmax > Fth. In this case use extension of fatigue life curve for design.
May define acceptable risk of exceedance for limited number of cycles of Fsrmax.
Fatigue - Design