## Slide 1
Teaching Modules for
Steel Instruction
BEAM
AISC Manual – 16th Edition
ANSI/AISC 360-22
Developed by Scott Civjan
University of Massachusetts, Amherst

## Slide 2
Beam Members:
  Chapter F: Design of Members for Flexure
  Chapter G: Design of Members for Shear
  Chapter I: Design of Composite Members
  Part 3: Design Charts and Tables
  Chapter B: Local Buckling Classification

## Slide 3
  Chapter F:
  Design of Members for Flexure

## Slide 4
fb = 0.90 (Wb = 1.67)
  Flexural Strength

## Slide 5
The Specification assumes that the following failure modes have minimal interaction and can be checked independently from each other:
  Lateral Torsional Buckling (LTB)
  Flange Local Buckling (FLB)
  Shear
  Flexural Strength

## Slide 6
Local Buckling:
  Criteria in Table B4.1
  Strength in Chapter F: Flexure
  Strength in Chapter G: Shear
  Flexural Strength

## Slide 7
Local Buckling Criteria
Slenderness of the flange and web, l, are used as criteria to determine whether buckling would control in the elastic or inelastic range, otherwise the plastic moment can be obtained before local buckling occurs.
Criteria p and r are based on plate buckling theory.
For W-Shapes
FLB,  = bf /2tf pf = , rf =
WLB,  = h/tw pw = , rw =
  Flexural Strength

## Slide 8
  p “compact”
Mp is reached and maintained before local buckling.
fMn = fMp
p    r “non-compact”
Local buckling occurs in the inelastic range.
f0.7My ≤ fMn < fMp
 > r “slender element”
Local buckling occurs in the elastic range.
fMn < f0.7My
  Flexural Strength
  Local Buckling

## Slide 9
Mr = 0.7FySx
Mp = FyZx
lp
Equation F3-1 for FLB:
lr
l
Mn
Equation F3-2 for FLB:
Local Buckling Criteria
Doubly Symmetric I-Shaped Members
Note: WLB not shown. See Spec. sections F4 and F5.

## Slide 10
Mr = 0.7FySx
Mp = FyZx
lp
Equation F3-1 for FLB:
lr
l
Mn
Equation F3-2 for FLB:
Local Buckling Criteria
Doubly Symmetric I-Shaped Members
Rolled W-shape sections are dimensioned such that the webs are compact and flanges are compact in most cases. Therefore, the full plastic moment usually can be obtained prior to local buckling occurring.
Note: WLB not shown. See Spec. sections F4 and F5.
Notes: 10

## Slide 11
The following slides assume:
  Compact sections
  Doubly symmetric members and channels
  Major axis bending
  Flexural Strength
Notes: This corresponds to simply supported beams which include a floor slab. The majority of beams fall into this easy to design category.

## Slide 12
Only consider LTB as a potential failure mode prior to reaching the plastic moment.
LTB depends on unbraced length, Lb, and can occur in the elastic or inelastic range.
If the section is also fully braced against LTB,
Mn = Mp = FyZx Equation F2-1
When members are compact:
  Flexural Strength

## Slide 13
Mp = FyZx Equation F2-1
Mr = 0.7FySx
Lp = Equation F2-5
Lr = Equation F2-6
Equation F2-7
ry =
For W shapes
c = 1 (Equation F2-8a)
ho = distance between flange centroids
When LTB is a possible failure mode:
Values of Mp, Mr, Lp and Lr are tabulated in Table 3-2

## Slide 14
Equation F2-2
Mr
Mp
Mn
Equation F2-3 and F2-4
Lb
Plastic LTB
Inelastic LTB
Elastic LTB
Lp
Lr
Lb
Lateral Brace
M = Constant (Cb=1)
Lateral Torsional Buckling
Strength for Compact
W-Shape Sections
X
X

## Slide 15
If Lb > Lr,
Mn = FcrSx ≤ Mp Equation F2-3
Where Equation F2-4
If Lp < Lb  Lr,
Equation F2-2
Note that this is a straight line.
If Lb  Lp,
Mn = Mp
Assume Cb=1 for now

## Slide 16
Results are included only for:
W-shapes typical for beams
Fy = 50 ksi
Cb = 1
Plots of Mn versus Lb for Cb = 1.0 are tabulated,
Table 3-10
  Flexural Strength

## Slide 17
To compute Mn for any moment diagram,
Mn = Cb(Mn(Cb1))  Mp
Mn = Cb(Mn(Cb1))  Mp
(Mn(Cb1)) = Mn, assuming Cb = 1
Cb, Equation F1-1
  Flexural Strength

## Slide 18
Mmax = absolute value of maximum moment in unbraced section
MA = absolute value of moment at quarter point of unbraced section
MB = absolute value of moment at centerline of unbraced section
MC = absolute value of moment at three-quarter point of unbraced section
X
X
MA
MB
MC
Mmax
Shown is the section of the moment diagram between lateral braces.
  Flexural Strength
Notes: Note that Cb calculation results differ based on location of lateral bracing and shape of moment diagram

## Slide 19
X
X
X
X
X
Example
Consider a simple beam with differing lateral brace locations.
Note that the moment diagram is unchanged by lateral brace locations.
M
M
X – lateral brace location
  Flexural Strength
Notes: Note that Cb calculation results differ based on location of lateral bracing and shape of moment diagram

## Slide 20
Cb approximates an equivalent beam of constant moment.
X
X
Mmax
X
X
Mmax/Cb
M
M/2
M
M
M
Cb=1.0
Cb=1.25
Cb=1.67
Cb=2.3
M
  Flexural Strength
Notes: As the moment gradient increases, Cb increases, which also increases Mn
One can think of Cb transforming the maximum moment to an equivalent constant moment value for design purposes.

## Slide 21
Lateral Torsional Buckling
Strength for Compact W-Shape Sections
Effect of Cb
Mr
Mp
Mn
Lb
Lp
Lr
Cb=1
  Flexural Strength

## Slide 22
Lateral Torsional Buckling
Strength for Compact W-Shape Sections
Effect of Cb
Mr
Mp
Mn
Lb
Lp
Lr
Cb=1
  Flexural Strength
Cb>1
Notes: 22

## Slide 23
Lateral Torsional Buckling
Strength for Compact W-Shape Sections
Effect of Cb
Mr
Mp
Mn
Lb
Lp
Lr
Cb=1
  Flexural Strength
Cb>1
Limited by Mp
Notes: 23

## Slide 24
  Chapter G:
  Shear Strength

## Slide 25
Nominal Shear Strength
Vn = 0.6FyAwCv1 Equation G2-1
0.6Fy = Shear yield strength per Von Mises Failure Criteria
Aw = area of web = dtw
Cv1 = reduction factor for shear buckling
  Shear Strength
  Without Tension Field Action

## Slide 26
For a rolled I-shaped member
If
Then fv = 1.00 (W = 1.50) and
Cv1 = 1.0 Equation G2-2
Vn = 0.6FyAw (shear yielding) (Cv1 = 1.0)
  Shear Strength
  Without Tension Field Action

## Slide 27
For all other I-shaped members:
fv = 0.90 (W = 1.67)
When
Equation G2-3
When
Equation G2-4
  Shear Strength
  Without Tension Field Action

## Slide 28
kv = 5.34 if no stiffeners are present or if
a = clear distance between transverse stiffeners
h = clear distance between flanges minus fillet on a rolled shape
Equation G2-5
  Shear Strength
  Without Tension Field Action

## Slide 29
Deflections :
  There are no serviceability requirements in AISC Specification.
  L1. states limits “shall be chosen with due regard to the intended function of the structure” and “shall be evaluated using appropriate load combinations for the serviceability limit states.”