## Slide 1
Teaching Modules for
Steel Instruction
BEAM THEORY SLIDES
Developed by Scott Civjan
University of Massachusetts, Amherst

## Slide 2
BEAM: Structural member subjected to bending and shear.
Ma
Va
Mb
Vb
Notes: If also includes axial loads – handle as Beam Column – see Module #3
Typically horizontal members of a frame
Support gravity loads and distribute forces to columns
Also can provide column end restraint, distribute resistance to lateral loads

## Slide 3
Yield and Plastic Moments

## Slide 4
Moment can be related to stresses, , strains, , and curvature, .
Stress strain law -
Initially assume linearly elastic, no residual stresses
(for elastic only).
Plane sections remain plane -
Strain varies linearly over the height of the cross section (for elastic and inelastic range).
Assumptions:
Yield and Plastic Moments

## Slide 5
Strain
Stress
Fu
Fy
E
ey
.001 to .002
eu
.1 to .2
esh
.01 to .03
er
.2 to .3
Stress vs. Strain
Esh

## Slide 6
Strain
Stress
E
ey
.001 to .002
eu
.1 to .2
esh
.01 to .03
er
.2 to .3
Stress-strain law
Esh
Elastic-Perfectly Plastic
Assumed in Design
Fu
Fy

## Slide 7
Strain
Stress
E
ey
.001 to .002
eu
.1 to .2
esh
.01 to .03
er
.2 to .3
Stress-strain law
Esh
Elastic-Perfectly Plastic
Assumed in Design
Fu
Fy
Initially we will review behavior in this range

## Slide 8
Plane sections remain plane.
Beam Theory
Yield and Plastic Moments
Notes: This allows for relationship between distance, strain, and stress through the cross section.
While variations will exist near boundaries, connections, etc. this is generally valid due to the ductile nature of steel.
8

## Slide 9
P = A = 0
Fi = A
Fi = 0
M = yA
M = yiFi
yi
dA
Centroid
Elastic Neutral Axis, ENA
Yield and Plastic Moments
Notes: For any shape we can set up equilibrium – the centroid is the elastic neutral axis (ENA).
This is the neutral axis during elastic loading for all shapes, but after yielding occurs it is only the neutral axis for sections loaded about an axis of symmetry.

## Slide 10
M
M
y
e
f
ymax
smax
ENA
Beam Theory
smax
Elastic Behavior:
Strain related to stress by Modulus of Elasticity, E
s = Ee
Yield and Plastic Moments
Notes: 10

## Slide 11
Beyond yield -
Stress is constant,
Strain is not related to stress by Modulus of Elasticity, E
Strain
Stress
Fy
E
eY
Beam Theory
Yield and Plastic Moments
Notes: 11

## Slide 12
Beyond yield -
Stress is constant,
Strain is not related to stress by Modulus of Elasticity, E
Strain
Stress
Fy
E
eY
Beam Theory
Yield and Plastic Moments
Now, consider what happens once some of the steel yields.
Notes: 12

## Slide 13
Increasing e
ey
Increasing s
Fy
Fy
Theoretically, reached at infinite strain.
Beam Theory
y
f
y
Beyond Elastic Behavior
Notes: The far right stress diagram, with essentially all of the section at yield stress, corresponds to the PLASTIC MOMENT (Mp). Due to ductile nature of steel, this can be reached in a typical section without fracture of the extreme fibers.
NOTE THAT stress=Mc/I IS NOT VALID
13

## Slide 14
Elastic Neutral Axis = Centroid
Plastic Neutral Axis –
If homogenous material (similar Fy), PNA divides Equal Areas, A1+A2/2.
For symmetric homogeneous sections, PNA = ENA = Centroid
Beam Theory
A1
A2
ENA
A1
y
x
A2/2
PNA
A1
A1
A2/2
x
yp
Yield and Plastic Moments
Notes: Use this slide to work an example for a symmetric shape
14

## Slide 15
Beam Theory
Yield Moment, My = (Ix/c)Fy = SxFy
Sx = Ix/c
c = y = distance to outer fiber
Ix = Moment of Inertia
Plastic Moment, Mp = ZxFy
Zx = AyA
For homogenous materials,
Zx = A iyi
Shape Factor = Mp/My
Yield and Plastic Moments
A1
A2
ENA
A1
y
x
A2/2
PNA
A1
A1
A2/2
x
yp
Notes: Use this slide to work an example for a symmetric shape
15

## Slide 16
Elastic Neutral Axis = Centroid
Plastic Neutral Axis ≠ Centroid
PNA divides equal forces in compression and tension.
If all similar grade of steel
PNA divides equal areas.
PNA
Beam Theory
A1
ENA
y
A2
A1
yp
A2
Yield and Plastic Moments
Notes: Use this slide to work an example of a non-symmetric shape
16

## Slide 17
Beam Theory
Plastic Moment, Mp = ZxFy
Zx = AyA = A iyi,
for similar material throughout the section.
Shape Factor = Mp/My
Yield Moment, My = (Ix/c)Fy = SxFy
Sx = Ix/c
c = y = distance to outer fiber
Ix = Moment of Inertia
PNA
A1
ENA
y
A2
A1
yp
A2
Yield and Plastic Moments
Notes: Use this slide to work an example of a non-symmetric shape
17

## Slide 18
With residual stresses, first yield actually occurs before My.
Therefore, all first yield
equations in the specification reference
0.7FySx
This indicates first yield 30% earlier than My.
For 50 ksi steel this indicates an expected residual stress of
(50 * 0.3) = 15 ksi.
Yield and Plastic Moments

## Slide 19
Moment
Mp
EI
curvature, f
My
Consider what this does to the Moment-Curvature relationship
Beam Theory
Yield and Plastic Moments
Notes: Moment-curvature relationship is as shown for a beam
When Residual Stresses are considered, yield will occur prior to the yield moment My.
Yield initiates at Mr, with a decrease in stiffness at all points up until Mp is reached.
Note that the maximum strength is not changed, but the behavior leading up to this directly affects potential failure modes.
19

## Slide 20
Beam Theory
Moment
Mp
EI
curvature, f
My
Consider what this does to the Moment-Curvature relationship
Yield and Plastic Moments
Including Residual Stresses
Notes: Moment-curvature relationship is as shown for a beam
When Residual Stresses are considered, yield will occur prior to the yield moment My.
Yield initiates at Mr, with a decrease in stiffness at all points up until Mp is reached.
Note that the maximum strength is not changed, but the behavior leading up to this directly affects potential failure modes.
20

## Slide 21
Lateral Torsional Buckling
(LTB)

## Slide 22
LTB occurs along the length of the section.
Result is lateral movement of the compression flange and torsional twist of the cross section.
Compression flange tries to buckle as a column.
Tension flange tries to stay in place.
Lateral Torsional Buckling
Notes: Animations or demonstrations are very helpful in showing this failure mode.

## Slide 23
Lb is referred to as the unbraced length.
Braces restrain EITHER:
Lateral movement of compression flange or
Twisting in torsion.
Ma
Va
X
X
X
X
Lb
X’s denote lateral brace points.
Lateral Torsional Buckling
Mb
Vb

## Slide 24
Handout on Lateral Bracing
Lateralbeambracing.pdf

## Slide 25
FACTORS IN LTB STRENGTH
  Lb - the length between beam lateral bracing points.
  Cb - measure of how much of flange is at full compression within Lb.
  Fy and residual stresses (1st yield).
  Beam section properties - J, Cw, ry, Sx, and Zx.
Lateral Torsional Buckling
Notes: Where:
E= modulus of elasticity (29000 ksi)
G= Elastic Shear modulus (11500 ksi)
A= Area (in2)
Sx= elastic section modulus
Iy= moment of inertia about the y axis
J= St. Venants torsion constant (in4)
Cw= Warping torsion constant (in6)

## Slide 26
The following sections have inherent restraint against LTB
for typical shapes and sizes.
  W shape bent about its minor axis.
  Box section about either axis.
  HSS section about any axis.
For these cases LTB typically does not occur.
Lateral Torsional Buckling

## Slide 27
Local Buckling

## Slide 28
Flange is restrained by the web at one edge.
28
Failure is localized at areas of high stress
(maximum moment) or imperfections.
Local Buckling is related to Plate Buckling
Notes: 28

## Slide 29
Flange is restrained by the web at one edge.
Failure is localized at areas of high stress
(maximum moment) or imperfections.
Local Buckling is related to Plate Buckling
Notes: 29

## Slide 30
Flange is restrained by the web at one edge.
Failure is localized at areas of high stress
(maximum moment) or imperfections.
Local Buckling is related to Plate Buckling
Notes: 30

## Slide 31
Local Buckling is related to Plate Buckling
Failure is localized at areas of high stress
(maximum moment) or imperfections.
Web is restrained by the flange at one edge, web in tension at other.
Partial Restraint from Flange
Partial Restraint from Web in Tension

## Slide 32
Local Buckling is related to Plate Buckling
Failure is localized at areas of high stress
(maximum moment) or imperfections.
Web is restrained by the flange at one edge, web in tension at other.
Partial Restraint from Flange
Partial Restraint from Web in Tension
Notes: 32

## Slide 33
Local Buckling is related to Plate Buckling
Failure is localized at areas of high stress
(maximum moment) or imperfections.
Web is restrained by the flange at one edge, web in tension at other.
Partial Restraint from Flange
Partial Restraint from Web in Tension
Notes: 33

## Slide 34
Handout on Plate Buckling
PlateBuckling.pdf

## Slide 35
If a web buckles, this is not necessarily a final failure mode. Significant post-buckling strength of the entire section may be possible (see advanced topics).
One can conceptually visualize that a cross section could be analyzed as if the buckled portion of the web is “missing” from the cross section.
Advanced analysis assumes that buckled sections are not effective, but overall section may still have additional strength in bending and shear.

## Slide 36
Local Web Buckling Concerns
Bending in the plane of the web;
  Reduces the ability of the web to carry its share of the bending moment (even in elastic range).
Support in vertical plane;
  Vertical stiffness of the web may be compromised to resist compression flange downward motion.
Shear buckling;
  Shear strength may be reduced.

## Slide 37
Shear Strength

## Slide 38
Shear limit states for beams
Shear Yielding of the web:
Failure by excessive deformation.
Shear Buckling of the web:
Slender webs (large d/tw) may buckle prior to yielding.
Shear Strength

## Slide 39
Shear Stress,  = (VQ)/(Ib)
   = shear stress at any height on the cross section
  V = total shear force on the cross section
  Q = first moment about the centroidal axis of the area between the extreme fiber and where  is evaluated
  I = moment of inertia of the entire cross section
  b = width of the section at the location where  is evaluated
Shear Strength

## Slide 40
Handout on Shear Distribution
ShearCalculation.pdf
Shear Strength
Notes: This example shows why a W-shape can be designed independently for shear and moment, as the shear stresses are low in the flange, where the bending stresses are highest. Also note that for a simple span the maximum shear and moments occur at different locations along the span.

## Slide 41
Shear stresses generally are low in the flange area
(where moment stresses are highest).
For design, simplifying assumptions are made:
1) Shear and Moment stresses are independent.
2) Web carries the entire shear force.
3) Shear stress is simply the average web value.
i.e. web(avg) = V/Aweb = V/dtw
Shear Strength
Notes: Basis for the 1st is the distribution from the shear calculation handout.

## Slide 42
Yield defined by Mohr’s Circle
Yield defined by Mohr’s Circle
Shear Yield Criteria
Shear Strength

## Slide 43
Von Mises Yield defined by maximum distortion strain energy criteria (applicable to ductile materials):
For Fy = constant for load directions
Specification uses 0.6 Fy
Shear Yield Criteria
Shear Strength
Notes: For Von Mises criteria the energy of distortion is set equal to the failure for yielding in uniaxial tension. This results in shear yield criteria of approximately 0.6 the value of the tensile yield stress.

## Slide 44
Von Mises Failure Criterion
(Shear Yielding)
When average web shear stress V/Aweb = 0.6Fy
V = 0.6FyAweb
Shear Strength

## Slide 45
V
V
V
V
t
t
V
V
C
V
V
T
Shear Buckle
Shear buckling occurs due to diagonal compressive stresses.
Extent of shear buckling depends on h/tw of the web (web slenderness).
Shear Strength

## Slide 46
V
V
If shear buckling controls a beam section, the plate section which buckles can be “stiffened” with stiffeners. These are typically vertical plates welded to the web (and flange) to limit the area that can buckle. Horizontal stiffener plates are also possible, but less common.
No Stiffeners
Stiffener spacing = a
Potential buckling restrained by stiffeners
Potential buckling restrained by web slenderness
Shear Strength
Notes: Note that for shear stiffeners (as opposed to bearing type) the stiffener does not need to be welded to both flanges, which reduces the cost.

## Slide 47
When the web is slender, it is more susceptible to web shear buckling. However, there is additional shear strength beyond when the web buckles.
Web shear buckling is therefore not the final limit state.
The strength of a truss mechanism controls shear strength called “Tension Field Action.”
Beam Theory
Shear Strength
V
V
Shear Buckling of Web
Notes: Tension Field Action is a post buckling mechanism that is relied on to increase the overall shear strength. For very slender webs this post-buckling strength is significant.
This strength is often relied upon in built up beam sections.
Stiffeners must be properly designed to carry the compression forces – in addition to out of plane stiffness criteria for typical shear stiffener design.
47

## Slide 48
V
V
When the web is slender, it is more susceptible to web shear buckling. However, there is additional shear strength beyond when the web buckles.
Web shear buckling is therefore not the final limit state.
The strength of a truss mechanism controls shear strength called “Tension Field Action.”
Beam Theory
Shear Strength
Tension can still be carried by the Web.
Notes: Tension Field Action is a post buckling mechanism that is relied on to increase the overall shear strength. For very slender webs this post-buckling strength is significant.
This strength is often relied upon in built up beam sections.
Stiffeners must be properly designed to carry the compression forces – in addition to out of plane stiffness criteria for typical shear stiffener design.
48

## Slide 49
V
V
When the web is slender, it is more susceptible to web shear buckling. However, there is additional shear strength beyond when the web buckles.
Web shear buckling is therefore not the final limit state.
The strength of a truss mechanism controls shear strength called “Tension Field Action.”
49
Beam Theory
Shear Strength
Compression can be carried by the stiffeners.
Tension can still be carried by the Web.
Notes: Tension Field Action is a post buckling mechanism that is relied on to increase the overall shear strength. For very slender webs this post-buckling strength is significant.
This strength is often relied upon in built up beam sections.
Stiffeners must be properly designed to carry the compression forces – in addition to out of plane stiffness criteria for typical shear stiffener design.
49

## Slide 50
V
V
Beam Theory
Shear Strength
Compression can be carried by the stiffeners
Tension can still be carried by the Web
For Tension Field Action to be effective the truss forces must be resisted at each node point.
Therefore , end panels are not effective, nor are widely spaced stiffeners, nor panels that are not well restrained around their perimeter.
Notes: Tension Field Action is a post buckling mechanism that is relied on to increase the overall shear strength. For very slender webs this post-buckling strength is significant.
This strength is often relied upon in built up beam sections.
Stiffeners must be properly designed to carry the compression forces – in addition to out of plane stiffness criteria for typical shear stiffener design.
50

## Slide 51
Beam Deflections

## Slide 52
Elastic behavior (service loads).
Limits set by project specifications.
Beam Deflections

## Slide 53
Typical limitation based on
Service Live Load Deflection
Typical criteria:
Max. Deflection, d = L/240, L/360, L/500, or L/1000
L = Span Length
Beam Deflections
Notes: Note that deflections are “serviceability” concern, so No Load factors should be used in calculations.

## Slide 54
INCLUDE REFERENCE MATERIAL:
AISC DESIGN GUIDE# 3: Serviceability Design Considerations for Steel Buildings (2nd Edition)

## Slide 55
Calculate deflection in beams from expected service dead load.
Result is a straight beam after construction.
Beam Deflections: Camber
Provide deformation in beam equal to a percentage of the dead load deflection and opposite in direction. It is important not to over-camber.
Specified on construction drawings.
Notes: Camber= curvature applied to a beam during fabrication to allow it to be relatively straight (no deflection) when dead loads are applied (self weight, floor slab) – this allows for a flat floor of consistent depth in a completed structure. Note that this is not an exact process, so camber calculations to the nearest ½ inch are usually sufficient.

## Slide 56
Beam without Camber
Beam Theory
Notes: 56

## Slide 57
Results in deflection in floor under Dead Load.
This can affect thickness of slab and fit of non-structural components.
d
Beam Theory
Notes: 57

## Slide 58
d
Beam Theory
d
Results in deflection in floor under Dead Load.
This can affect thickness of slab and fit of non-structural components.
Beam with Camber
Notes: 58

## Slide 59
Beam Theory
Results in deflection in floor under Dead Load.
This can affect thickness of slab and fit of non-structural components.
d
d
Cambered beam counteracts service dead load deflection.
Notes: 59

## Slide 60
Beam Vibrations

## Slide 61
INCLUDE REFERENCE MATERIAL:
AISC DESIGN GUIDE#11: Floor Vibration Due to Human Activity