## Slide 1
Computing Mn of a Partially Composite Beam
be = effective width of the concrete slab
hr = height of deck ribs (concrete in deck ribs is not considered effective)
tc = thickness of concrete above the deck
d = depth of steel beam
a = depth of compression block in concrete
Y2 = distance from top of steel beam to a/2 (the location of conc. Comp. force, Cc)
Y1 = distance from the top of steel beam to the PNA in the flange.
Qn = nominal strength of one stud shear connector
Case 1a) Plastic Neutral Axis in the Steel Beam Flange
Cc
PNA
Fy
0.85f’c
tc
hr
d
be
a
Ts
Fy
Y1
Y2
Cs
Fy
Cc
0.85f’c
2Cs
Equivalent stress distribution.
2Fy
T
bf
Cc + Cs = Ts Cc + 2Cs = T

## Slide 2
Computing Mn of a Partially Composite Beam
Case 1a) Plastic Neutral Axis in the Steel Beam Flange
Cc
PNA
Fy
0.85f’c
tc
hr
d
be
a
Ts
Fy
Y1
Y2
Cs
Fy
Cc
0.85f’c
2Cs
Equivalent stress distribution.
2Fy
T
bf
Using the equivalent stress distribution and taking moments about Cs:
For Case 1a, PNA in beam flange: Cc + Cs = Ts Cc + 2Cs = T
Y1 = distance from top of steel beam to the PNA in flange.
Y1 ≤ tf, flange thickness.
Cc = ΣQn (strength/stud X no. of studs from M=0 to M=Mmax)
Cc = 0.85f’cbea (a ≤ tc)
T = AsFy

## Slide 3
Using the equivalent stress distribution and taking moments about d/2:
Computing Mn of a Partially Composite Beam
Case 1b) Plastic Neutral Axis in the Steel Beam Web
PNA
Ts
Fy
hr
d
be
Cs
Fy
Fy
T/2
Equivalent stress distribution.
Fy
T/2
Y1
Y2
d/2
Cc + Cs = Ts Cc + T/2 = T/2 + Ts1
Cc = ΣQn (strength/stud X no. of studs from M=0 to M=Mmax)
Cc = 0.85f’cbea (a ≤ tc)
Ts1 = 2twFy(d/2 – Y1)
T = AsFy
Y1 = distance from top of steel beam to the PNA in web.
Y1 ≥ tf, flange thickness.
Fy
Ts1
For Case 1b, PNA in beam web:
Cc
0.85f’c
tc
be
a
Cc
0.85f’c